## Slide 1: FYS4260 - Microsystems and electronic packaging and interconnection technologies

## Slide 2: Lab info
Lab room: 204
10 students at the time
Room is available Mon-Fri. from 9-17 (-21)
Laboratory supervisor:
  Halvor Strøm: halvor.strom@fys.uio.no
  Tuesday from 9-16
  David Bang: davidmb@fys.uio.no
  Thursday from 9-16

## Slide 3: Setup – Cadstar I
Start CADSTAR Design Editor
Click ”Tools” => ”Options”
Screenshot of CADSTAR Design Editor

## Slide 4: Setup – Cadstar II
Select ”Library path” tab and click ”Add”
Type in or find in browser: W:\CADlibs\Cadstar\LIBRARY-FYS4260
Click ”OK”
Adding component library

## Slide 5: Setup – Cadstar III
Delete local component library
Finished adding FYS4260 prepared component library and deleted local library

## Slide 6: Setup – Cadstar IV
Load predefined templates
  Color files
  Template files
  User files
Set design directories
  Initial Design Directory
  Manufacturing Output
  Output Report Files
Remember to save workspace to preserve these settings for next time.
Screenshot of CADSTAR template setup

## Slide 7: Setup – Cadstar V
Setup Network Licensing Host:
Name: volt
Port: 1700

## Slide 8: Project start
Click ”File” and ”new”
Press ”Schematic Design” => select ”DefFYS4260..”=> ”OK”
Press ”OK” again and input ”Design Title”and ”Attributes”

## Slide 9: Schematic – Placing components
There are 2 ways of adding components
  Searching component name/value/attributes
  Picking component directly from library

## Slide 10: Schematic – Adding components II
Searching for components
  Press ”Search”
  Type ”*search word*” => ”OK”
Naming conventions:
0 ohm -> 0R0
47 ohm -> 47R0
4.5 Kohm -> 4K5
100nF - > 100n / 0.1u
3.4pF -> 3p4

## Slide 11: Schematic – Adding components III
Searching for components
  Press ”Browse” => ”OK”
  Select library and pick a component

## Slide 12: Schematic – Component definition
SYMBOL (Schematic)
Parts description
Footprint (PCB component)
SYMBOL
(Schematic)
PARTS-LIB
FOOTPRINT
(PCB)

## Slide 13: Schematic – Adding a power source
The circuit is powered by a 9V battery
Add a bypass capacitor for noise cancelling
Add an electrolyte/tantal capacitor for ripple and dips
And a voltage regulator..?

## Slide 14: Schematic – Connections and Colour Codes I
There are 3 types of connections
  POWER (Blue)
  GND (Purple)
  Signal (White)
Signal is set as default, POWER/GND must be defined the first time

## Slide 15: Schematic - Hierarchy blocks

## Slide 16: Schematic – Verifying design
Produce a report on unconnected component pins
  Click ”Tools” => ”Reports” => ”unused components”.
”unused components” report

## Slide 17: Links
Help guides:
  CADSTAR’s Do-It-Your-Self: W:\CADlibs\Cadstar\cadstar_121_expressdiy.pdf
  PCB Help: W:\CADlibs\Cadstar\PCBSelfTeach.pdf
  Schematic Help: W:\CADlibs\Cadstar\SCMSelfTeach.pdf
Report guide: http://tid.uio.no/kurs/fys4260/Scientific_writing-Ohlckers.pdf