## Slide 1: INF5350 – CMOS Image Sensor Design
Lecture 1 – CMOS camera systems overview

## Slide 2: Lecture 1 objectives
Overview how cameras work from light in to digital images out
Introduce topics to be covered in more detail later in the course

## Slide 3: Literature
  Only lecture notes are obligatory
  Reference:
  Nakamura et al:
    Ch. 1 (background material)
    Ch. 2 (until 2.1.2)

## Slide 4: Picture definition
Defn: 2D array of pixels (picture elements) each containing numbers (R+G+B or Y+U+V) to describe the pixel color and its brightness (intensity)
Zoom-in on LCD screen w/RGB pixels
Zoom-in to see individual pixel elements
Every pixel outputs Red+Green+Blue light

## Slide 5: RGB vs YUV color representation
U-V color plane
(Y=0.5)
YUV image
along with its
Y,
U,
V components.
Mixing primary colors (RGB)
RGB
YUV

## Slide 6: RGB to YUV, and vice-versa

## Slide 7: The electromagnetic spectrum
Wavelength
λ=400nm
λ=700nm
Visible
Infrared
Radio waves
UV
X-ray
Gamma
λ=

## Slide 8: Camera system
Digital Image Processing (ISP)
System Controller
Data bus
USB
Memory card
LCD monitor
Lens
Shutter
CIS
CIS = CMOS image sensor

## Slide 9: CIS chip architecture example

## Slide 10: Camera signal chain
LENS CORRECTION
DEFECT PIXEL CORRECTION
BLACK LEVEL COMPEN-SATION
COLOUR PROCESSING

## Slide 11: Illustration of micro-lens array
Micro-lenses improve light sensitivity and sharpness
Purpose is to focus incoming light to the middle of the pixel to avoid light leakage (losses) to neighbouring pixels and/or light loss due to reflections off transistors, metal routing, etc
0.8-5um diameter
(=pixel size)

## Slide 12: Frontside illuminated (FSI) CMOS sensor
3-6um
1-3um
Passivering
Micro lense
Color filter
P-doped silicon
Photon detection
Metal routing
12

## Slide 13: Backside illuminated (BSI) CMOS sensor
Incoming light
’Backside’
’Frontside’
1-2um
After CMOS process, wafer is thinned to ca 5um and placed on a carrier wafer. Then CFA and ulenses are deposited.
Better light sensitivity than FSI (Frontside illuminated) sensor
BSI technology important for small pixel sizes <6um
BSI avoids the need for the light to go through these routing layers

## Slide 14: FSI vs BSI

## Slide 15: CMOS-sensor with ’Bayer’ color filter array
Repetitive 2x2 pattern (RGBG)
CFA = color filter array
Photo
diode

## Slide 16: CFAs used in CMOS image sensors
The choice of CFA depends on application requirements, i.e. light sensitivity vs colour accuracy vs spatial resolution

## Slide 17: CMOS pixel array (4T pixels)
Cfd
PD
SF
Cfd
PD
SF
Cfd
PD
SF
Cfd
PD
SF
Ibias
Ibias
Vcol0
Vcol1
Cfd node converts photon charges (e-) into voltage (DV)
SF drives voltage on output column bus.
SF current source is outside array (one per column)

## Slide 18: Conversion gain
Charge detection scheme:
Assuming number of electrons capture = Selectrons
Voltage swing at FD node: DVFD = CG Selectrons
Conversion gain:
q = 1.6 x 10-19 C
CFD = floating diffusion capacitance
FD

## Slide 19: Sequential row readout
Vcol1
Vcol2
Vcol3
Vcol4
3V
0V
0V
Step-1: enable selected row
Step-2: sample each column value (Vcoln)
Step-3: disable row
Step-4: increment row address, repeat above steps
0V

## Slide 20: Sequential row readout
0V
0V
0V
3V
Vcol1
Vcol2
Vcol3
Vcol4

## Slide 21: Sampling and digitizing output from pixel array
A/D
G
+
-
SHS
OpAmp
C2
C1
Vcol<n>
SHR
SHS
G x DV
DV
DV
Vcol<n>
DV proportional to number of photons in the pixel
Vrst
Vsig
Vsig
Vrst
Dout
SHR

## Slide 22: Black level compensation (BLC)
ADC output values non-zero even if pixel output signal is zero
  Any clipping at 0DN in ADC leads to non-linear sensor data (asymmetric histogram curve)
  Offset voltage (Voffset) added to pixel signal before A/D converter
  Additional offset comes from dark current generation when operating at elevated temperatures and/or long integration times
Image processing functions (e.g. defect pixel correction, lens correction, HDR, and color processing) rely on ‘linear’ pixel values, i.e. proportional to incoming light level (without offsets). Hence, BLC is needed.
BLC uses optical black pixels (shielded with opaque material) to estimate average black level value
Average across many pixels to remove noise
NB. Important black level is same across the array (no shading)

## Slide 23: Black level compensation (BLC)
Before BLC
After BLC
Light level (a.u.)
Pix. value (a.u.)
0
2Nbits
0
Light level (a.u.)
Pix. value (a.u.)
0
2Nbits
0
Offset pedestal
Offset due to dark current and/or analogue offset
Offset removed. Pixel values are now ‘linear’, ie proportional to light level

## Slide 24: CIS readout chain
Typical values:
Vpix_rst=2V, Vpix_sig=1-2V, G=1x-16x, Voffset=50mV, Vref=1V, N=10
Fixed black level independent of Tint, Temp, and Gain
Dark current BLC component proportional to exposure time and gain, and doubles every ~7degC.

## Slide 25: Example of optical black rows/columns

## Slide 26: Lens shading correction

## Slide 27: Defect pixel correction
Objective: Detect and correct abnormal (damaged) pixels
Can be done automatically on-the-fly and/or in mass production by writing (x,y) positions into non-volatile memory
Correct by interpolation from neighboring pixels
DPC complexity and quality depends on power and chip size budget
Example image from Wikipedia

## Slide 28: Color interpolation
Purpose: to generate R+G+B for each pixel position
Three common methods:
  Nearest neighbor interpolation
  (Bi)Linear interpolation
  Bi-Cubic spline interpolation

## Slide 29: Nearest neighbor interpolation
x: distance to pixel i
f(x): weighting factor

## Slide 30: Linear and Bi-Linear interpolation
Linear:
Bi-Linear (x and y direction):
x: distance to pixel i
f(x): weighting factor

## Slide 31: Bi-Cubic spline interpolation
Cubic
spline:
Bi-cubic spline:

## Slide 32: HW implementation cost

## Slide 33: Color correction
Purpose: Improve color accuracy by compensating for crosstalk between R-G-B pixels
Crosstalk due to imperfect colour filters, reflections, charge leakage, etc.
Matrix ‘A’ = Color correction matrix (CCM)
3x3 matrix with fixed values typically stored in non-volatile memory
This condition ensures average brightness remains unchanged
Red to green crosstalk, a1
Blue to green crosstalk, a3

## Slide 34: Camera colour characterization
[r, g, b]
[R, G, B]
Captured raw image (after CIP)
Target results
After color correction (CCM)

## Slide 35: HDR combines multiple pictures
Two captures combined into one picture with correct exposure everywhere!

## Slide 36: Tone mapping / gamma curve
Purpose: (i) Map output image to 8b RGB display, (ii) Data compression
Popular mapping scheme: y(x) = xg
  g ~0.45 typical value
Global TM
  Same function on entire image
  Reversable
Local TM
  Function changes accross image
  Better image quality
  Non-reversable

## Slide 37: Tone mapping example

## Slide 38
Thanks!

## Slide 39
ADDITIONAL SLIDES FOR INFORMATION

## Slide 40: CIS signal chain (single A/D architecture)

## Slide 41: Digital Camera-on-a-chip in CMOS
Pixel array
A/D converters
Timing and control
ISP, PLLs, Vrefs, TempSensor, I/O, etc

## Slide 42: Block diagram of CMOS image sensor
2MP, ¼”, 15fps
Source: ISSCC ’09

## Slide 43: Fabrication of integrated circuits in CMOS
i) From Si-ingot to Si-substrate (300mm)
iii) Dicing wafers into die
iv) From die to chips in package
ii) 300mm wafers
with CMOS die

## Slide 44: Active research topics in the field of CIS design (selected examples)
Multi-layer stacked chip camera modules
  Pixel, ADCs, ISP, memory, I/O in separate layers
  More parallelism, similar to human visual system
High dynamic range (HDR) capture
  HDR involves combining high/low sensitivity captures
  How to avoid LED flicker issues
  How to avoid motion artefacts
Reducing power consumption
  Typical CIS power consumption is 100-500mW
    Difficult to maintain as array size (resolution) keeps increasing
  Need <10mW to enable battery driven IoT cameras, pill cameras, door bells, etc.
  Stacking paradigm shift to enable lower power
Improved infrared response for LL imaging, etc

## Slide 45: CCD vs CMOS
Foton til elektron
konvertering
Ladning til
spenning konvertering

## Slide 46: Analog/Digital conversion (Volts to bits)
Input voltage
1111=15d
1110
1101
1100
1011
1010
1001
1000
0111
0110
0101
0100
0011
0010
0001
0000