## Slide 1: IN5350 – CMOS Image Sensor Design
Lecture 2 – 3T and 4T pixels

## Slide 2: Contents
Introduction
3T pixel
  Circuit
  Timing diagram (capture and readout)
  Hard vs soft reset
4T pixel circuit and timing diagram

## Slide 3: Camera signal chain
Photodiode
This lecture

## Slide 4: 3x3 pixel array with address decoders
Row (y) decoder
Column (x) decoder
Output
Diode
Diode
Diode
Diode
Diode
Diode
Diode
Diode
Diode
Row 0
Row 1
Row 2

## Slide 5: 3T pixel
RST
ROW
VPD
RST
VRST
VDD
Mrst
Msf
Msel
ROW
VCOL
Ipd
Tint
PD
VCOL
V1
V2
N.A.

## Slide 6: 3T pixel
Photodiode (PD) is reverse bias and the n-side is ‘floating’ during image capture. PD acts as a capacitor. Its voltage drops proportionally to the photocurrent.
Mrst is a reset switch. Its purpose is to pre-charge the photodiode to a starting voltage VRST before image capture starts.
Msf serves as a common drain amplifier (aka source follower). Note its current source is placed outside the pixel array and shared by all pixels on that column.
Msel is a row select switch. When enabled the source follower of that pixel will drive the column line (aka bit line from RAM terminology).

## Slide 7: 3T pixel image capture process
Step-1: Pulse RST (pre-charge PD to VRST)
  Removes any photon-charge from previous capture
Step-2: Wait for exposure time to elapse
Step-3: Turn ON Msel
  To enable pixel SF to drive column bus
Step-4: Sample column voltage (V1=Vout)
  This voltage is called the ‘signal level'
Step-5: Pulse the RST switch
  Forces PD back to its original pre-charge level (VRST)
Step-6: Sample column voltage (V2=Vout)
Final result: DV = V2 – V1

## Slide 8: 3T pixel remarks
Compatible with off-the-shelf CMOS devices
  CFA and ulens deposition available from other vendors
PD composed of NW/P-sub
Use thick oxide NFETs to withstand 3V operation

## Slide 9: Hard reset vs soft reset
Vth in NFETs typically 0.5-0.8V
Mrst turns off gradually as VPD increases which leads to too low VGS
This means VPD will never reach VRST during pre-charge but instead asymptotically move towards RST-Vth (aka ‘soft reset’)
Soft vs Hard reset of PD
  Pros: sqrt(2) lower kTC-noise; simplest implementation
  Cons: incomplete reset causes charge lag (traces of charge from previous frame occurs in current frame)
Hard reset obtained by boosting RST voltage to VRST+Vth or by setting VRST < VDD-Vth

## Slide 10: Motivation for delta-sampling (V1-V2)
Question
  Ref above timing diagram, if PD is always pre-charged to the same voltage (ie VRST with hard reset or VRST-Vth with soft reset) then why waste time sampling this pre-charge level (V2) when reading the pixel?
Answer
  SF output dc level depends on Vth which can vary significantly (+/- tens of mV) from pixel to pixel and cause Fixed Pattern Noise (FPN) artefacts. Delta sampling mitigates this issue.

## Slide 11: Fixed pattern noise (FPN) examples
Pixel FPN from SF Vth variation
Mitigated by delta-sampling
Vertical FPN from Vth variation in current source
Mitigated by delta-sampling

## Slide 12: 4T pixel circuit and timing
RST
VRST
VDD
Mrst
Msf
Msel
ROW
COL
TX
Mtx
RST
ROW
VFD
Tint
VCOL
V1
V2
N.A.
TX
PD
FD

## Slide 13: 4T pixel remarks
PD behaves similarly to 3T pixel, ie always reverse biased and generates charge proportional to the light level.
Mtx is called a transfer gate. Its purpose is to enable/disable charge flow between PD and FD.
Mrst reset switch controls (i) pre-charge of PD and (ii) pre-charge of FD node during CDS readout.
Msf serves as a source follower as in 3T pixel.
Msel is a row select switch. Same as in 3T pixel.

## Slide 14: 4T pixel image capture process
Step-1: Pulse RST and TX simultaneously
  Resets PD. Removes any photon-charge from previous capture
  N part of diode is 100% depleted. Hence, VPD after pre-charge is fixed at Vpin (defined by ND implants) with zero kTC-noise.
Step-2: Wait for exposure time to elapse
Step-3: Assert ROW
  To enable pixel voltage on column bus
Step-4: Pulse RST (keeping TX off)
Step-5: Sample column output voltage (V1=Vout)
  This corresponds to the FD reset level
Step-6: Pulse the TX switch (0.5-1us pulse width, typical value)
  PD photo-electrons move to FD which has a higher potential
  Once charge transfer is complete VPD returns to Vpin
Step-7: Sample column voltage (V2=Vout)

## Slide 15: 4T pixel remarks
N region in the PD is 100% depleted after pre-charge => no kTC-noise
Shallow P+ layer (connected to ground) on top of N region to absorb any dark current generated at the Si/SiO2 interface => MUCH lower dark current (10x-1000x).
  P+ pinning layer requires extra process steps compared to off-the-shelf CMOS
In addition, special engineering of the transfer gate (TX) implants is needed to ensure low DC and that all PD electrons move across to FD without lagging behind causing image artefacts in the subsequent frame
Often, special engineering is also done with the SF device (typically buried channel device) to obtain best possible noise performance
Anti-blooming path via TX and RST, ie these devices must pass through electrons when PD is saturated

## Slide 16: Pixel sharing enables higher fill factor
2x2 sharing => From 4 to 7/4 devices/pixel
SF
SEL
VRST

## Slide 17: 3T vs 4T pixels
3T
Fully CMOS compatible
High noise (kTC, DC, ..)
Used in applications where S/N ratio is not important
2x1, 2x2, 2x3 sharing enables fewer devices per pixel
4T
Pixel implants different from the CMOS devices
Extremely low noise (no KTC, low DC, ..)
Used in nearly all of today’s digital cameras
2x1, 2x2, 2x3 sharing enables fewer devices per pixel