## Slide 1: Project schedule
Task/milestone | Start | Finish
Chose topic/scope | 16-Sep | 20-Sep
Create project plan (tasks, milestones, schedule) | 20-Sep | 27-Sep
MS1 – project plan approved by Johannes | 30-Sep | 30-Sep
Study literature on the topic | 27-Sep | 4-Oct
Design/simulation | 4-Oct | 25-Oct
Write up prelim report (inc references, design, results) | 25-Oct | 29-Oct
MS2 – submit preliminary report to Johannes | 29-Oct | 29-Oct
Design/simulation | 29-Oct | 15-Nov
Write up final report (incl references, design, results) | 15-Nov | 22-Nov
MS3 – submit final report to Johannes & presentation | 22-Nov | 22-Nov
MS4 – grading (pass/fail) by Johannes & Tohid | 22-Nov | 22-Nov
Exam | 28-Nov 2019 | 

## Slide 2: Course project
Project size: 40-60hrs total
Schedule: see next slide
Grade: pass/fail (must pass to take exam).
Topic&field is optional:
  Analog design (e.g. SPICE: pixel array and readout circuits)
  Digital design (e.g. RTL: readout timing, image signal processing)
  Algorithm design (Matlab/Python: BLC, DPC, AEC, AWB)
Deliverables: (i) Project plan, (ii) Project report, (iii) Presentation
Groups of max 2 persons is allowed, but clearly differentiate who did what in the project.
For access to nanolab in 5th floor email your name, username, and card number to Olav Stanly Kyrvestad <olavky@ifi.uio.no>
All SW (Cadence, Matlab, etc) available on all machines at IFI, as well as via remote login from external computer

## Slide 3: IN5350 – CMOS Image Sensor Design
Lecture 4
Section I – Readout timing
Section II – Readout circuits

## Slide 4: IN5350 – CMOS Image Sensor Design
Lecture 4
Section I – Readout timing
Section II – Readout circuits

## Slide 5: Contents
Introduction
Section I
  Electronic rolling shutter
  Blanking time (HB and VB)
Section II
  Row decoder/driver
  Voltage boosting and driving
  Analog CDS
  Digital CDS

## Slide 6: CIS block diagram
Pixel array
Column ADCs
Line memory
ISP
Output FIFO
Timing and control logic
Row decoder

## Slide 7: Analog vs Digital CDS
Analog CDS
  Sample&Hold(Vrst & Vsig) => OpAmp => deltaV => ADC
  Pros: faster (less ADC activity), lower readnoise floor
  Cons: vertical FPN due to column offset variations (parasitics)
Digital CDS
  Vrst => ADC, Vsig => ADC, digital calculation of ‘deltaV’ (ie number of photons captured)
  Pros: less analogue circuit complexity, best VFPN performance (analog offsets subtracted off)
  Cons: need 2x faster ADC, root(2) higher noise when subtracting the two samples to get ‘deltaV’
Commercially imagers use predominantly digital CDS

## Slide 8: 4T pixel readout
RS
RST
SHR
TG
SHS
ADC_busy
Trow<i>
Trow<i+1>
ACDS
DCDS

## Slide 9: Electronic rolling shutter
‘Readout’ and ‘Reset’ pointers move in parallel from row to row
‘Readout’ points at output row to be sampled, digitized and sent to the output FIFO
‘Reset’ points at row to be reset (pre-charged), thus starting a new capture
Readout and reset pointers increment after completion. Total rowtime is ‘Trow’.
Exposure time (Texp) = Nrows x Trow, where Nrows=number of rows between Reset pointer and Readout pointer
Readout
Reset
Texp
Row<j>
(Texp/Trow rows)
Row<j+Texp/Trow>

## Slide 10: Frame timing
Pixel row0
Tint
Trow
time
Row readout time
Exposure time
Let Nrows=total number of pixel rows
Time to readout all rows (aka frame time)
  Tframe = Nrows x Trow
  Frame rate = 1/Tframe
  E.g. 50Hz video => Tframe = 20ms
Not to scale
Tframe usually msec
Trow usually usec
Pixel row1
Pixel row2
Pixel row3
Pixel row4
Tframe

## Slide 11: Frame timing (short exposure time)
Pixel row0
Tint
Trow
time
Tint : exposure time adjustable between one row and 1/fvideo
Pixel should be in reset mode during idle time in order to prevent PD saturation and blooming of charge into neighbouring pixels
Pixel row1
Pixel row2
Pixel row3
Pixel row4
Tframe
idle
idle

## Slide 12: Frame timing
pixels ‘idling’
pixels ‘idling’

## Slide 13: Contents
Introduction
Section I
  Electronic rolling shutter
  Blanking time (HB and VB)
Section II
  Row decoder/driver
  Voltage boosting and driving
  Analog CDS
  Digital CDS

## Slide 14: Electron beam scanning principle in old analogue TVs (cathode ray tubes)
Cathode Ray Tube
Raster scanning principle
Horizontal blanking time
i.e. electron beam OFF
Vertical blanking time, i.e. electron beam OFF

## Slide 15: Analogue NTSC video format

## Slide 16: Analogue NTSC video format

## Slide 17: Typical video frame definitions

## Slide 18: Contents
Introduction
Section I
  Electronic rolling shutter
  Blanking time (HB and VB)
Section II
  Row decoder/driver
  Voltage boosting and driving
  Analog CDS
  Digital CDS
  A/D converters

## Slide 19: Row decoder circuit example
VTX
VRST
VTX 0
VRST 0
VROWSELECT 0
VTX 1
VRST 1
VROWSELECT 1
VTX 2
VRST 2
VROWSELECT 2

## Slide 20: 3T CMOS Active Pixel Structure
Schematics
Layout
VDD
Vout
RST
Select
Detector
surface
RST

## Slide 21: Boosting
To keep ON resistance low in pixel switches (RST, RS, and TX) when/if their source/drain potentials get large, it is possible to ‘boost’ the gate voltage above VDD.
RST
2
1
VDD
VDD
2
1
1
1
CL
CB
Vboost = VDD(1+CB/(CB+CL))
Voltage across CL:
1: VL(1)=VDD
2. VL(2)=VL(1)+I dT/CL
=VDD(1+CB/(CB+CL))

## Slide 22: Boost circuit with non overlapping clock generator

## Slide 23: Alternative boosting circuits (charge pumps)
Charge pump doubler. Cp delivers charge to Co to compensate for current load on the output
Dickson doublers

## Slide 24: ADCs for CMOS image sensors
Serial readout
  w/Pipeline ADC
Column-parallel readout
  w/Ramp ADC
  w/SAR-ADC

## Slide 25: Correlated Double Sampling
Vout
TG
RST
RowSel
VDD
Vbias
FD
Source follower
RowSel
RST
TG
VFD
or Vout
SHR
SHS
DV

## Slide 26: Serial readout architecture
Advantages:
Small die size
Uniform response
Disadvantages:
Low framerate
Column bus limits noise and power performance
Serial readout suitable for small arrays and moderate framerates
Typically pipeline ADC

## Slide 27: Serial readout architecture (example)
Image sensor
ASP+Address decoder
ASP
Address decoder
27

## Slide 28: Serial readout architecture
Source: Cho et al, IISW’07
Large capacitance output bus not good for noise and power (speed)

## Slide 29: 3.3V 12 BIT 6.3 MS/S PIPELINED ADC
Source: Hamami et al, ISCAS04

## Slide 30
Source: Johansson et.al, ISSCC 2011

## Slide 31: Agenda
Pixels and readout circuits
Serial readout
  w/Pipeline ADC
Column-parallel readout
  w/Ramp ADC
  w/SAR-ADC

## Slide 32: Column Parallel Readout
Advantages:
Fast readout
Low noise
Low power
Disadvantages:
Large chip size
Difficult to implement at small pixel pitch
Column non-uniformity

## Slide 33: Ramp ADC column circuit
SHS
SHR
Pixel output
Reference: Snoeij et al, IEEE J. of SSC, 2006

## Slide 34: Slope ADC
Vramp
Clk

## Slide 35: Ramp ADC remarks
Most widely used in commercial CMOS imagers
Relatively low circuit complexity
Low noise bandwidth
Small area (ramp generator shared)
One ADC per column with shared input ramp
Requires a lot of clocks (2Nbits) per conversion
  Used by counter
  Typically accompanied by on-chip PLL (100-1000MHz)

## Slide 36: Successive Approximation ADC (aka SAR ADC)
SAR
DAC
Control logic
+
-
Comparator
S/H
Vref
Vin
Binary output
Vref = max input voltage (all 1s)
Vref(b0/16+b1/8+b2/4+b3/2)
b3
b2
b1
b0
Successive Approximation Register
Ex: Vin=0.7V, Vref=1V
=> Output=1011

## Slide 37: 12b SAR ADC with split capacitor DAC
Source: Solhusvik et al, IISW’17, Japan

## Slide 38: SAR ADC remarks
Most widely used ADC in the general industry (but ramp ADC dominates in imagers)
Faster than ramp ADC because it requires only Nbits clocks per conversion (vs 2Nbits)
  12b@1us typical performance in commercial sensors
Besides the comparator and output latch, an N-bit capacitor DAC is needed in every column
  Challenging column layout
Typically limited to 12-14bits, but higher resolution versions do exist (not in imagers)