## Slide 1: INF5350 – CMOS image sensor design
Lecture 5 – Noise and modelling S/N
27-September-2019

## Slide 2: Agenda
Project milestone status
Takeaways from previous lecture&exercises
Noise and S/N in CMOS image sensors

## Slide 3: Project schedule
Task/milestone | Start | Finish
Chose topic/scope | 16-Sep | 20-Sep
Create project plan (tasks, milestones, schedule) | 20-Sep | 27-Sep
MS1 – project plan approved by Johannes | 30-Sep | 30-Sep
Study literature on the topic | 27-Sep | 4-Oct
Design/simulation | 4-Oct | 25-Oct
Write up prelim report (inc references, design, results) | 25-Oct | 29-Oct
MS2 – submit preliminary report to Johannes | 29-Oct | 29-Oct
Design/simulation | 29-Oct | 15-Nov
Write up final report (incl references, design, results) | 15-Nov | 22-Nov
MS3 – submit final report to Johannes & presentation | 22-Nov | 22-Nov
MS4 – grading (pass/fail) by Johannes & Tohid | 22-Nov | 22-Nov
Exam | 28-Nov 2019 | 
✅

## Slide 4: Key takeaways from previous lectures and exercises
Linearity of pixel values should be within +/-0.5% for good image quality (no color artifacts, etc)
Pixel source follower is linear to within 0.5-1% but only in the range where the devices are in saturation
  controllable with device sizing and bias current
In addition, load capacitance and settling time must be considered, i.e. SF settling to within 99% of final value with maximum DV input voltage
  controllable with device sizing and bias current

## Slide 5: Linearity sometimes impacted by settling
Light level (a.u.)
Pixel value (DN)
Settling to 99% of final value
RST=on
Vrst
Signal levels, Vsig
Vsf_out
TX=on
e
Non linearity
Linear

## Slide 6: Noise sources in image sensors

## Slide 7: Two noise categories
1. Temporal noise
2. Fixed pattern noise
Temporal noise: random disturbance which changes every time a capture is taken
Fixed pattern noise: does NOT change with time (ie fixed pattern superimposed on the image)

## Slide 8: Temporal noise example
Temporal noise changes randomly with time (ie for every capture)
Example pixel row profile:
Column position
Pixel value

## Slide 9: Photon shot noise
Temporal noise that changes randomly from pixel to pixel and capture to capture (even if light level is constant)
Follows Poisson’s probability distribution:
p(x) = probability of x incidents (e.g. x photons detected in a pixel during Tint),
e = natural logarithm base (~2.72),
µ = mean value, i.e. statistical average of x, ie

## Slide 10: Property of Poisson process: variance equals the mean (µ)
Signal/Noise of ideal photon detector ():
Ex: if a pixel detects an average of 100photons, then S/N=10 (20dB)

## Slide 11: Poisson distribution plots at various mean values (µ)
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0.36792 | 0.36792 | 0.18396 | 0.06132 | 0.01533 | 0.003066 | 0.000511 | 7.3e-05 | 9.1249e-06 | 1.0139e-06 | 1.0139e-07 | 9.2171e-09 | 7.6809e-10 | 5.9084e-11 | 4.2203e-12 | 2.8135e-13 | 1.7585e-14 | 1.0344e-15 | 5.7466e-17 | 3.0245e-18 | 1.5123e-19
 | 0.13536 | 0.27073 | 0.27073 | 0.18048 | 0.090242 | 0.036097 | 0.012032 | 0.0034378 | 0.00085945 | 0.00019099 | 3.8198e-05 | 6.945e-06 | 1.1575e-06 | 1.7808e-07 | 2.544e-08 | 3.392e-09 | 4.24e-10 | 4.9882e-11 | 5.5424e-12 | 5.8341e-13 | 5.8341e-14
 | 0.0067414 | 0.033707 | 0.084268 | 0.14045 | 0.17556 | 0.17556 | 0.1463 | 0.1045 | 0.065312 | 0.036284 | 0.018142 | 0.0082465 | 0.003436 | 0.0013215 | 0.00047198 | 0.00015733 | 4.9165e-05 | 1.446e-05 | 4.0167e-06 | 1.057e-06 | 2.6426e-07
 | 4.5447e-05 | 0.00045447 | 0.0022724 | 0.0075745 | 0.018936 | 0.037873 | 0.063121 | 0.090173 | 0.11272 | 0.12524 | 0.12524 | 0.11385 | 0.094879 | 0.072984 | 0.052131 | 0.034754 | 0.021721 | 0.012777 | 0.0070985 | 0.003736 | 0.001868
µ=1
µ=2
µ=10
Number of incidences (e.g. photons or electrons)
Probability of occurrance (no unit)

## Slide 12: Photon shot noise examples
Ref: Wikipedia
m=0e-
m=1e-
m=2e-
m=4e-
m=10e-
m=30e-
m=100e-
m=1000e-
m=10000e-

## Slide 13: Fixed pattern noise (FPN)
FPN (also called nonuniformity) is the time invariant spatial variation in pixel output values under uniform illumination (incl total darkness) due to device and parameter variations (mismatches) across the sensor
Fixed for one sensor, but the nonuniformity pattern changes randomly from sensor to sensor. Hence, the ‘noise’ term.
E.g. vertical or horizontal stripes, white pixels, black pixels, shading, …

## Slide 14: FPN compensation
FPN in pixels can be compensated digitally
For instance, dark FPN (ie FPN under zero illumination) can be removed by subtracting a dark image from regular captures
  But FPN compensation too costly in commercial products. Instead, sensor must be designed for FPN to be invisible to human eye => 10x below temporal noise
Original picture
Dark image
After compensation
A
B
A - B

## Slide 15: Dark current = both temporal noise and fixed noise (FPN)
Thermally generated electrons (or holes) in the pixel. Adds to the photo-generated signal charge and thus creates a pedestal offset.
Problem is that dark current is a random process (Poissonian, just like photons). Hence, it appears as noise in the picture or video at high temperatures and/or long integration times.
Mean value accross the array (Ndark) is a constant value and not defined as noise, since not random. In fact, it can be measured and subtracted from the pixel values (Black.
Standard deviation (sdark) is temporal noise

## Slide 16: Thermal noise
Thermal agitations of electrons within a resistance (fundamental in all circuits)
Random variation for every capture
Example row profile in darkness:

## Slide 17: Signal/noise model

## Slide 18: Introduction
Signal/noise ratio (S/N or SNR) is an essential quality performance parameter of any sensor
SNR quantifies how precise, accurate, reliable, trustworthy, .. the sensor output value is
Modelling SNR is important when making design desicions such as pixel size, circuit topology, ADC resolution, etc.
This section covers SNR modelling, incl correlated double sampling, and the impact of FPN

## Slide 19: Outline
Define signal and noise for CMOS image sensors
Create model of S (from photons to bits)
Create model of N (shot noise, RN, ADC..)
Create model of CDS sampling process
Discuss how FPN influences SNR

## Slide 20: Signal-to-noise ratio (SNR)
Input signal (a.u.)
Output signal (a.u.)
Sensor
Input signal
Output signal&noise
σ=rms noise=std.dev.
µ
S/N in dB: 20log()
µ=mean sig

## Slide 21: Model of signal chain (multiple blocks)
G1, σ1
G2, σ2
G3, σ3
Sin/ σin
Sout/σout
S: signal
Gi: gain of module i
σi: rms noise added by ith module (uncorrelated with the others)
NB! Noise sources added together. However, only in power (V2) domain, not in voltage domain due to the noise voltage (and/or noise current) being random with zero mean value.

## Slide 22: Pixel+ADC model
CGfd, σkTC
Gsf, σsf
Gadc, σadc
Sin/ σin
Sout/σout
Floating diffusion
Source follower
A/D converter
Se-: number of photo-electrons generated by photodiode
Sout: ADC output signal (DN or LSBs)
σkTC, σsf: rms noise voltage from FD and SF, respectively (V rms)
σadc: rms noise from ADC after gain (LSB rms)
Gadc: ADC conversion gain, (2^Nbits-1)/Vref_adc (LSB/V)
CGfd: floating diffusion conversion gain (V/e-)
Eliminated with
CDS
Readnoise, RN
Photon shot noise

## Slide 23: Calculating rms noise value (σ) from noise spectrum, N(f)
Integrate N(f) across all frequencies to get σ
N(f): noise spectrum (V2/Hz)
σ: rms noise voltage (V)

## Slide 24: Frequency domain representation
H(f)N(f)
Sin(f)
Nin(f)
Sin(f): input signal spectrum (V2/Hz)
H(f): transfer function of any linear time-invariant system, e.g. pixel, amplifier, filter, ADC, CDS, ..
N(f): noise spectrum of additive noise source inside H(f), e.g. Johnson noise or 1/f-noise from resistors or transistors (V2/Hz)
Sout(f)
Nout(f)

## Slide 25: Signal chain in frequency domain
H1(f)N1(f)
Sin(f)
Nin(f)
H(f): transfer function of any linear time-invariant system, e.g. pixel, amplifier, filter, ADC, CDS, ..
N1(f), N2(f), N3(f): noise spectrum of noise sources (V2/Hz)
H2(f)N2(f)
H3(f)N3(f)
Sout(f)
Nout(f)

## Slide 26: CIS signal chain from photons to bits
CIP
CCM

## Slide 27: Pixel light flux for a given scene illumination
Esc=scene irradiation (W/m/m2)
ρsc=scene reflectivity (no unit)
F=lense F-nummer (=f/Dobj)
Dobj= lens aperture (m)
f = lens focal length (m)
Ad=detector area (m2)
λ=light wavelength (m)
Ed=detector irradiation (W/m/m2)

## Slide 28: Calculation of pixel value after ADC
SADCout=output value (DN aka LSBs)
Esc(λ)=spectral irradiation (W/m/m2)
ρsc(λ)=scene reflectivity (no unit)
Tint=camera exposure time (s)
F=lense F-nummer (=f/Dobj)
h=Plancks constant (6.6x10-34 J s)
c=speed of light (3x108 m/s)
Apix=detector area (m2)
λ=light spectral wavelength (m)
CGpix=conversion gain (V/e-)
Gsf=source follower gain (no unit)
Nbits=ADC resolution (no unit)
Vadc_ref=ADC saturation level (V)

## Slide 29: Temporal noise sources
Photon shot noise =>µ=Se-, σ=sqrt(Nph)
  Nph: mean value of photons
Dark current noise =>µ=Ndc, σ=sqrt(Ndc)
  Ndc: mean value of dark current electrons
Read noise =>µ=0, σ=RN (V rms)
  RN: temporal noise in darkness from pixel+ADC

## Slide 30: Read noise sources
Temporal noise at zero illumination
Read noise =>µ=0, σ=RN
  RN: rms noise floor in dark from pixel+ADC
  Pixel source follower noise sources
    White noise
    1/f noise
  ADC noise
    White noise
    1/f noise
    Quantization noise =>µ=0, σ=1LSB/sqrt(12)

## Slide 31: Example of 4T pixel output signal with noise
kT/C noise
Reset level (Vrst)
White noise and 1/f noise, Npix(f)
Signal level (Vsig)
Vpix(t)
t
RST
TX

## Slide 32: White noise and 1/f noise in transistors
N(f)
N(f)=k
N(f)=1/f
N(f)=1/f2