## Slide 1: INF5350 – CMOS image sensor design
Lecture 6 – Modelling S/N ratio
4-October-2019

## Slide 2: Agenda
Project milestone status
Takeaways from previous lecture&exercises
Modelling S/N ratio

## Slide 3: Project schedule
Task/milestone | Start | Finish
Chose topic/scope | 16-Sep | 20-Sep
Create project plan (tasks, milestones, schedule) | 20-Sep | 27-Sep
MS1 – project plan approved by Johannes | 30-Sep | 30-Sep
Study literature on the topic | 27-Sep | 4-Oct
Design/simulation | 4-Oct | 25-Oct
Write up prelim report (inc references, design, results) | 25-Oct | 29-Oct
MS2 – submit preliminary report to Johannes | 29-Oct | 29-Oct
Design/simulation | 29-Oct | 15-Nov
Write up final report (incl references, design, results) | 15-Nov | 22-Nov
MS3 – submit final report to Johannes & presentation | 22-Nov | 22-Nov
MS4 – grading (pass/fail) by Johannes & Tohid | 22-Nov | 22-Nov
Exam | 28-Nov 2019 | 
✅
✅
✅
✅

## Slide 4: Key takeaways from previous lecture
Temporal noise vs Fixed pattern noise
Photon flux and electron flux are random Poisson processes
  Mean value (μ) = Variance (σ2) = (RMS value, σ)2
Independent noise sources can be summed quadratically
  stotal = sqrt(s12+ s22 + s32 + ..)

## Slide 5: SNR model based on s for each block
How to model s for pixels, gain amplifiers, filters, ADCs, etc?
CGfd, σkTC
Gsf, σsf
Gadc, σadc
Sin/ σin
Sout/σout
Floating diffusion
Source follower
A/D converter

## Slide 6: Modelling noise in frequency domain
Nin(f): noise power density at input (V2/Hz)
Nout(f): noise power density at output (V2/Hz)
H(f): transfer function of a linear time-invariant system, e.g. pixel, amplifier, filter, ADC, CDS, ..
H(f)
Nin(f)
Nout(f) (V2/Hz)
(V rms)

## Slide 7: Noise spectral density at pixel SF output
Npix(f) = k1 + k2/f + k3/f2 (V2 / Hz)
Measured noise spectrum at the output of a CCD source follower at -40C. CMOS source followers look similar. White noise (k1) dominates at high frequencies, typically above 1-10MHz.
Npix(f)

## Slide 8: Digital CDS model
Low-pass filter
Sample&Hold
A/D
ALU
Vref
Signal, Vpix
Noise, Npix
Signal, DV
Noise, s
d(t) = delta-dirac function models the ADC input signal sampling
Nbit = number of ADC bits (typically 10b-12b)
Vref = ADC reference voltage (typically 1V at 1x gain)
TCDS = time interval between sampling of reset level and signal level

## Slide 9: Fourier transfer of DCDS process
))
)
(i.e. Vrst-Vsig)

## Slide 10: DCDS transfer function example
Chart: freq (Hz)
Low frequency signals & noise attenuated

## Slide 11: DCDS with LP filter for noise limitation
Input
A/D and digital CDS
Output
Low-pass filter

## Slide 12: DCDS w/LP filter transfer function example
Roll-off due to low-pass filter
Chart: freq (Hz)

## Slide 13: Output noise after digital CDS
(LSB2)

## Slide 14: Correlated Multi-Sampling (CMS)
Sample Vrst and Vsig twice and take average to reduce noise (need twice as fast ADCs)
Low-pass filter
A/D
ALU
/2
CDS

## Slide 15: CMS S/N model
/2
}
(LSB2)

## Slide 16: Example of Poisson distributed random values (e.g. photons and dark current)
Mean(A) = 2 => sigma(A) = 1.4
Mean(B) = 10 => sigma(B) = 3.2
Mean(A+B) = 12 => sigma(A+B) = 3.5

## Slide 17: Noise from color crosstalk
R’=a1R+a2G+a3B e.g. 1.35R-0.2G-0.15B
G’=b1R+b2G+b3B e.g. -0.05R+1.1G-0.05B
B’=c1R+c2G+c3B e.g. -0.05R-0.15G+1.2B
Matrix ‘A’ = Color correction matrix (CCM)
3x3 matrix with fixed values stored in non-volatile memory
Ref to green crosstalk, b1
Blue to green crosstalk, b3

## Slide 18: Noise from color crosstalk (cont.)
Green signal, G’ = b1R + b2G + b3B
Green noise, σG’2 = b12σR2 + b22σG2 + b32σB2
Assuming R=G=B=Se->>RN (photon noise limited)
The larger the CCM values, the lower the SNR. (same for blue and red pixels.)
NB! Above assumes b1+b2+b3=1 (unchanged brightness)

## Slide 19: Photoresponse non-uniformity
Fixed pattern noise
Several potential root causes
  Quantum efficiency variation due to manufacturing spread in the optical stack and/or in the PD implants
  Conversion gain (CG) variation due to parasitic capacitance variation
  Source follower gain variation due to Vth variation in active device
PRNU (in e- rms, V rms, or LSB rms) is proportional to the signal level
Therefore, it is usually quoted in terms of % rms of signal level
Let’s assume a signal level of 500e- and 1% rms PRNU. Then,

## Slide 20: SNR model w/FPN sources
Gasc, σasc
Sin/ σin
Sout/σout
Se: number of photo-electrons generated by photodiode
Sout: ADC output signal (DN or LSBs)
σPRNU: photoresponse non-uniformity (% rms)
σDSNU: dark signal non-uniformity (e- rms)
σvfpn: rms noise from vertical column FPN (LSB rms)
Gasc: conversion factor of analog signal chain, (LSB/e-)
CGfd: floating diffusion conversion gain (V/e-)
If Se >>1 => SNR=1/σPRNU

## Slide 21: Example noise curve
Chart: Light level (e-)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 2000 | 3000 | 4096 | 5000 | 6000 | 7490 | 7500 | 9000 | 12000 | 15000 | 20000 | 25000 | 29995 | 30500 | 44000 | 46000 | 59000 | 61000 | 90000 | 100000
noise (e- rms) | 3.1623 | 3.3167 | 3.4642 | 3.6058 | 3.742 | 3.8734 | 4.0006 | 4.1239 | 4.2436 | 4.36 | 5.3889 | 6.2522 | 7.0114 | 7.6974 | 8.3283 | 8.9157 | 9.4678 | 9.9905 | 10.4881 | 14.5945 | 17.8326 | 20.6155 | 23.1084 | 25.3969 | 27.5318 | 29.5466 | 31.4643 | 33.3017 | 49.0816 | 62.522 | 76.0442 | 86.6545 | 98.0255 | 114.4946 | 114.6037 | 130.8014 | 162.5085 | 193.6724 | 244.9673 | 295.8192 | 346.3726 | 351.474 | 487.4515 | 507.552 | 638.0509 | 658.1102 | 948.688 | 1048.8131
Photon shot noise dominated
PRNU dominated
RN=3e-

## Slide 22: Example SNR plot
Chart: Light level (e-)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 2000 | 3000 | 4096 | 5000 | 6000 | 7490 | 7500 | 9000 | 12000 | 15000 | 20000 | 25000 | 29995 | 30500 | 44000 | 46000 | 59000 | 61000 | 90000 | 100000
SNR (dB) | -10 | -4.3935 | -1.2497 | 0.90123 | 2.5173 | 3.8011 | 4.8594 | 5.7557 | 6.5302 | 7.2102 | 11.3906 | 13.6218 | 15.1251 | 16.2525 | 17.1519 | 17.8988 | 18.5368 | 19.0931 | 19.5861 | 22.7368 | 24.5182 | 25.7573 | 26.704 | 27.4674 | 28.1053 | 28.6517 | 29.1285 | 29.5507 | 32.2022 | 33.6218 | 34.6259 | 35.2236 | 35.7362 | 36.3139 | 36.3173 | 36.7526 | 37.3661 | 37.7805 | 38.2384 | 38.5383 | 38.7501 | 38.7681 | 39.1104 | 39.1455 | 39.3199 | 39.3406 | 39.5424 | 39.586
Photon shot noise dominated
PRNU dominated

## Slide 23: PRNU dominates over photon shot noise at high signal levels
PRNU for most sensors is <1% rms
Negligible at small signal levels (small FW) but becomes dominant at high signal levels
Chart: PRNU (% rms)
| 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012
PRNU/PN @1K | 0.031623 | 0.063246 | 0.094868 | 0.12649 | 0.15811 | 0.18974 | 0.22136 | 0.25298 | 0.2846 | 0.31623 | 0.34785 | 0.37947 | 0.4111 | 0.44272 | 0.47434 | 0.50596 | 0.53759 | 0.56921 | 0.60083 | 0.63246 | 0.66408 | 0.6957 | 0.72732 | 0.75895 | 0.79057 | 0.82219 | 0.85381 | 0.88544
PRNU/PN @10K | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2 | 2.3 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8
PRNU/PN @100K | 0.31623 | 0.63246 | 0.94868 | 1.2649 | 1.5811 | 1.8974 | 2.2136 | 2.5298 | 2.846 | 3.1623 | 3.4785 | 3.7947 | 4.111 | 4.4272 | 4.7434 | 5.0596 | 5.3759 | 5.6921 | 6.0083 | 6.3246 | 6.6408 | 6.957 | 7.2732 | 7.5895 | 7.9057 | 8.2219 | 8.5381 | 8.8544
PRNU/PN @1M | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28

## Slide 24: Example of picture with random noise
Possible noise sources in this picture:
Photon noise in ‘grey’ medium bright areas
Dark current (DC) in dark areas
Electronic circuit noise (read noise) in dark areas
Photoresponse-non-uniformity (PRNU) in bright areas

## Slide 25: Vertical fixed pattern noise (VFPN)
Example of column FPN (vertical FPN)
When VFPN is randomly distributed across columns, it can be modelled similarly to temporal noise:

## Slide 26: Signal, Noise and Dynamic Range
Source: Nakamura et.al.

## Slide 27: Key takeaways
Noise sources added together in power domain or variance (ie V2, I2, or s2)
CDS eliminates in-pixel kTC-noise and strongly attenuates low-frequency (1/f) noise
The larger the color correction matrix (CCM) values, the more shot noise is added to the pixel
FPN is calculated after removing (averaging) temporal noise. Thus, FPN relates to the image, not a single pixel.

## Slide 28: appendix

## Slide 29: Random variables
Discrete random variables modelled as probability mass function
  x is integer (example: number of photons or electrons in a Poisson process)
A continuous random variable (x real, e.g. analogue voltage) modelled as probability density function
  x is real (example: analogue voltage in a Gaussian process)

## Slide 30: Gaussian random variable
f(x)
s