# IN5520	     2020

# Exercises on shape representation

Problem 11.8 in G&W DIP3E, 11.15 in G&W DIP4E

Creating region objects using Matlab

In this practical exercise you will work your way through  preprocessing, segmentation, creating region objects, and computing simple shape descriptiors.

- Load the image ‘tall_noise10_backgr.png’ from

www.uio.no/studier/emner/matnat/ifi/in5520/h19/undervisningsmateriale/tall_noise10_backgr.png

The image contains number on a noisy background. The background has both low frequent background variations and high frequent noise.

- Try to filter out the high frequent noise using either a convolution low-pass filter or a median filter.

- Thresholding the image using a global threshold does not work as the image has varying background. We can either compute the threshold in a local window, or estimate the background and subtract it from the image. Try estimating the background using either a mean filter or a median filter with a very large size (applied to the result from point 2). The filter size should be so large that the filtered image only shows the background, not the numbers.

- Compute the difference between the filtered image and the noise-filtered from point 2. Is the result you got now suitable for global thresholding? Experiment with filter sizes.

- Threshold the image using a global threshold.

- Analyze how good the thresholding is : are the numbers connected? Do we have one connected component per number? What about the frame?

- Compute region objects in matlab and create a region label image to study how the regions correspond to numbers

b1 = bwlabel(bw);

cc=bwconncomp(b1);

ll = labelmatrix(cc);

regim = label2rgb(ll);

imshow(regim);

- Compute simple region properties using regionprops in matlab. Can you use region area to remove the frame and noisy segments?

- Create scatter plots between pairs of region properties using the function gscatter. Do you see what is noise or frame in the scatter plots?

d=regionprops(b1,'area','boundingbox','ConvexArea'…….); %Add more properties, see doc regionprops

feat1 = d.Area;

feat2 = d.BoundingBox;

gscatter(feat1,feat2);

# From 2012 Exam: Exercise 1: Chain Codes

You are given the 8-directional chain code and the object below, where black is object pixels.

- Chain code the boundary of the object clockwise from the upper left pixel.

- Which technique will make the code invariant to the choice of start point? 
Demonstrate this by starting at lower right pixel of the object.

- Which technique will make the code rotation invariant?
Demonstrate this by rotating the object π/2 counterclockwise and start at one of the same object pixels as above.

# Text boxes

0

2

3

1

5

4

6

7