## Slide 1: Preemptive Scheduling and Mutual Exclusion with Hardware Support
Thomas Plagemann
With slides from Otto J. Anshus & Tore Larsen (University of Tromsø) and Kai Li (Princeton University)

## Slide 2: Overview
Interrupts:
  Handling
  Software
  Hardware maskable & non-maskable
  Exceptions
A bit on scheduling
Hardware support for mutex
  Fischer algorithm
  Disable interrupts
  Test and Set Lock

## Slide 3: Preemptive Scheduling
Scheduler select a READY process and sets it up to run for a maximum of some fixed time (time-slice)
Scheduled process computes happily, oblivious to the fact that a maximum time-slice was set by the scheduler
Whenever a running process exhausts its time-slice, the scheduler needs to suspend the process and select another process to run (assuming one exists)
To do this, the scheduler needs to be running! To make sure that no process computes beyond its time-slice, the scheduler needs a mechanism that guarantees that the scheduler itself is not suspended beyond the duration of one time-slice. A “wake-up” call is needed

## Slide 4: Interrupts and Exceptions
Interrupts and exceptions suspend the execution of the running thread of control, and activates some kernel routine
Three categories of interrupts:
  Software interrupts
  Hardware interrupts
  Exceptions

## Slide 5: EFlags Register

## Slide 6: Interrupt Description Table Register (IDTR)
The 8088/8086 processor does not have an IDT register
IDT consists of 256 4 bye entries
Each entry specifies the start address of the interrupt service routine associated with the interrupt vector

## Slide 7: Real Mode Interrupt/Exception Handling
High level description
Processor actions

## Slide 8: Interrupt Handling in Real vs. Protected Mode
Real mode
  Each entry in interrupt table is 4 bytes long
  Start address of interrupt handler in segment:offset format
  Any program can use INT nn
Protected mode
  OS must restrict access to some routines that may be called through INT nn
  Handle some interrupts or exceptions by suspending current task and switching to another task
  Each entry in interrupt table is 8 bytes
  Calling program must have sufficient privilege to trigger a routine and must meet privilege level specified in Eflags[IOPL] to execute CLI and STI

## Slide 9: Software Interrupts
INT instruction
Explicitly issued by program
Synchronous to program execution
Example: INT 10h

## Slide 10: Hardware Interrupts
Set by hardware components (for example timer), and peripheral devices (for example disk)
  Timer component, set to generate timer-interrupt at any specified frequency! Separate unit or integral part of interrupt controller
Asynchronous to program execution
Non-maskable (NMI), and maskable interrupts.
  NMI are processed immediately once current instruction is finished.
  Maskable interrupts may be permanently or temporarily masked

## Slide 11: Maskable Interrupt Request
Some IO devices generate an interrupt request to signal that:
  An action is required on the part of the program in order to continue operation
  A previously-initiated operation has been completed with no errors encountered
  A previously-initiated operation has encountered an error condition and cannot continue

## Slide 12: Non-maskable Interrupt Requests
In the PC-compatible world, the processor’s non-maskable interrupt request input (NMI) is used to report catastrophic HW failures to the OS

## Slide 13: Exceptions
Initiated by processor
Three types:
  Fault: Faulting instruction causes exception without completing. When thread resumes (after IRET), the faulting instruction is re-issued. For example page-fault
  Trap: Exception is issued after instruction completes. When thread resumes (after IRET), the immediately following instruction is issued. May be used for debugging
  Abort: Serious failure. May not indicate address of offending instruction
Have used Intel terminology in this presentation. Classification, terminology, and functionality varies among manufacturers and authors

## Slide 14: I/O and Timer Interrupts
Overlapping computation and I/O:
  Within single thread: Non-blocking I/O
  Among multiple threads: Also blocking I/O with scheduling
Sharing CPU among multiple threads
  Set timer interrupt to enforce maximum time-slice
  Ensures even and fair progression of concurrent threads
Maintaining consistent kernel structures
  Disable/enable interrupts cautiously in kernel
CPU
Memory
Interrupt

## Slide 15: When to Schedule?
Process created
Process exits
Process blocks
I/O interrupt
Timer

## Slide 16: Process State Transitions
Running
Blocked
Ready
I/O completion interrupt
(move to ready queue)
Create
Terminate
(call scheduler)
Yield, Timer Interrupt
(call scheduler)
Block for resource
(call scheduler)
Scheduler
dispatch

## Slide 17
Process State Transitions (cont.)
P4
P3
P2
P1
P2
P1
ReadyQueue
P4
P3
BlockedQueue
Scheduler
Dispatcher
Trap Handler
Service
!
Current
Trap Return Handler
U s e r L e v e l P r o c e s s e s
KERNEL
MULTIPROGRAMMING
Uniprocessor: Interleaving (“pseudoparallelism”)
Multiprocessor: Overlapping (“true paralellism”)
PC
PCB’s
Memory resident part
(Process Table)
Running
Blocked
Ready
I/O completion interrupt
(move to ready queue)
Create
Terminate
(call scheduler)
Yield, Timer Interrupt
(call scheduler)
Block for resource
(call scheduler)
Scheduler
dispatch
Syscall

## Slide 18: Transparent vs. Non-transparent Interleaving and Overlapping
Non-preemptive scheduling (“Yield”)
  Current process or thread has control, no other process or thread will execute before current says Yield
    Access to shared resources simplified
Preemptive scheduling (timer and I/O interrupts)
  Current process or thread will loose control at any time without even discovering this, and another will start executing
    Access to shared resources must be synchronized

## Slide 19: Implementation of Synchronization Mechanisms
Concurrent Applications
Locks Semaphores Monitors
Load/Store Interrupt disable Test&Set
High-Level
Atomic API
Low-Level
Atomic Ops
Interrupt (timer or I/O completion), Scheduling, Multiprocessor
Send/Receive
Shared Variables
Message Passing

## Slide 20: Hardware Support for Mutex
Atomic memory load and store
  Assumed by Dijkstra (CACM 1965): Shared memory w/atomic R and W operations
  L. Lamport, “A Fast Mutual Exclusion Algorithm,” ACM Trans. on Computer Systems, 5(1):1-11, Feb 1987.
Disable Interrupts
Atomic read-modify-write
  IBM/360: Test And Set proposed by Dirac (1963)
  IBM/370: Generalized Compare And Swap (1970)

## Slide 21: A Fast Mutual Exclusion Algorithm (Fischer)
Repeat await <x=0>; <x := i>; <delay>; until <x = i>;
  use shared resource
<x := 0>;
Entry:
Exit
Critical Region
”While x ≠ 0 do skip;”
Or could block? How?
Executed by process no. i.
X is shared memory.
<op> is an Atomic Operation.
We are assuming that COMMON CASE will be fast and that all processes will get through eventually

## Slide 22: Disable Interrupts
CPU scheduling
  Internal events
    Threads do something to relinquish the CPU
  External events
    Interrupts cause rescheduling of the CPU
Disabling interrupts
  Delay handling of external events
    and make sure we have a safe ENTRY or EXIT

## Slide 23: Does This Work?
Kernel cannot let users disable interrupts
Kernel can provide two system calls, Acquire and Release, but need ID of critical region
Remember: Critical sections can be arbitrary long (no preemption!)
Used on uni-processors, but won’t work on multiprocessors
Acquire() {
disable interrupts;
}
Release() {
enable interrupts;
}
User Level

## Slide 24: Disabling Interrupts with Busy Wait
We are at Kernel Level!: So why do we need to disable interrupts at all?
Why do we need to enable interrupts inside the loop in Acquire?
Would this work for multiprocessors?
Why not have a “disabled” Kernel?
Acquire(lock) {
disable interrupts;
while (lock != FREE){
enable interrupts;
disable interrupts;
}
lock = BUSY;
enable interrupts;
}
Release(lock) {
disable interrupts;
lock = FREE;
enable interrupts;
}

## Slide 25: Using Disabling Interrupts with Blocking
When must Acquire re-enable interrupts in going to sleep?
  Before insert()?
  After insert(), but before block?
Would this work on multiprocessors?
Acquire(lock) {
disable interrupts;
while (lock == BUSY) {
insert(caller, lock_queue);
BLOCK;
} else
lock = BUSY;
enable interrupts;
}
Release(lock) {
disable interrupts;
if (nonempty(lock_queue)) {
out(tid, lock_queue);
READY(tid);
}
lock = FREE;
enable interrupts;
}

## Slide 26: Atomic Read-Modify-Write Instructions
What we want: Test&Set(lock):
  Returns TRUE if lock is TRUE (closed), else returns FALSE and closes lock.
Exchange (xchg, x86 architecture)
  Swap register and memory
Compare and Exchange (cmpxchg, 486 or Pentium)
  cmpxchg d,s: If Dest = (al,ax,eax), Dest = SRC; else (al,ax,eax) = Dest
LOCK prefix in x86
Load link and conditional store (MIPS, Alpha)
  Read value in one instruction, do some operations
  When store, check if value has been modified. If not, ok; otherwise, jump back to start
The Butterfly multiprocessor
  atomicadd: one processor can read and increment a memory location while preventing other processors from accessing the location simultaneously

## Slide 27: The TSL Instruction (1)
Figure 2-25. Entering and leaving a critical region using the TSL instruction.

## Slide 28: The XCHG Instruction
Figure 2-26. Entering and leaving a critical region using the XCHG instruction.

## Slide 29: The LOCK# Signal and Prefix in x86
Causes the CPUs to assert the LOCK# signal
Practically ensures exclusive use of the memory address in multiprocessors / multi-thread environments
Works with the following instructions:
Works only if all follow the rule:
BT, BTS, BTR, BTC (mem, reg/imm)
XCHG, XADD (reg, mem / mem, reg)
ADD, OR, ADC, SBB (mem, reg/imm)
AND, SUB, XOR (mem, reg/imm)
NOT, NEG, INC, DEC (mem)
Thread 1: lock inc ptr [edx] Thread 2: inc ptr [edx]

## Slide 30: A Simple Solution with Test&Set
Waste CPU time (busy waiting by all threads)
Low priority threads may never get a chance to run (starvation possible because other threads always grabs the lock, but can be lucky…): No Bounded Waiting ( a MUTEX criteria)
No fairness, no order, random who gets access
Acquire(lock) {
while (TAS(lock))
;
}
Release(lock) {
lock = FALSE;
}
{TAS := lock; lock := TRUE;}
INITIALLY: Lock := FALSE; /* OPEN */
Spin until lock = open
TAS (lock):

## Slide 31: Test&Set with Minimal Busy Waiting
Two levels: Get inside a mutex, then check resource availability (and block (remember to open mutex!) or not).
Still busy wait, but only for a short time
Works with multiprocessors
Acquire(lock) {
while (TAS(lock.guard))
;
if (lock.value) {
enqueue the thread;
  block and lock.guard:=OPEN; %Starts here after a Release()
}
lock.value:=CLOSED;
lock.guard:=OPEN;
}
Release(lock) {
while (TAS(lock.guard))
;
if (anyone in queue) {
dequeue a thread;
make it ready;
} else lock.value:=OPEN;
lock.guard:=OPEN;
}
CLOSED = TRUE OPEN = FALSE

## Slide 32: A Solution without Busy Waiting?
BUT: No mutual exclusion on the thread queue for each lock: queue is shared resource
    Need to solve another mutual exclusion problem
Is there anything wrong with using this at the user level?
    Performance
    “Block”??
Acquire(lock) {
while (TAS(lock)) {
enqueue the thread;
block;
}
}
Release(lock) {
if (anyone in queue) {
dequeue a thread;
make it ready;
} else
lock:=OPEN;
}

## Slide 33
Different Ways of Spinning
Perform TAS only when lock.guard is likely to be cleared
  TAS is expensive
while (TAS(lock.guard))
;
while (TAS(lock.guard)) {
while (lock.guard)
;
}
Always execute TAS

## Slide 34
Using System Call Block/Unblock
Block/Unblock are implemented as system calls
How would you implement them?
  Minimal waiting solution
Acquire(lock) {
while (TAS(lock))
Block( lock );
}
Release(lock) {
lock = 0;
Unblock( lock );
}

## Slide 35: Block and Unblock
Block (lock) { insert (current, lock_queue, last); goto scheduler (; }
Unblock (lock) { insert (out (lock_queue, first), Ready_Queue, last); goto scheduler; }
Ready_Queue
lock_queue
Current

## Slide 36: Summary
Interrupts
Scheduling
Hardware support for mutex
  Fischer algorithm
  Disable interrupts
  TSL instruction
Next week:
  Semaphores
  Event counters
  Monitors