## Slide 1: INF5063 – GPU & CUDA
Håkon Kvale Stensland
Simula Research Laboratory

## Slide 2: PC Graphics Timeline
Challenges:
  Render infinitely complex scenes
  And extremely high resolution
  In 1/60th of one second (60 frames per second)
Graphics hardware has evolved from a simple hardwired pipeline to a highly programmable multiword processor
1998
1999
2000
2001
2002
2003
2004
DirectX 6
Multitexturing
Riva TNT
DirectX 8
SM 1.x
GeForce 3
Cg
DirectX 9
SM 2.0
GeForceFX
DirectX 9.0c
SM 3.0
GeForce 6
DirectX 5
Riva 128
DirectX 7
T&L TextureStageState
GeForce 256
2005
2006
GeForce 7
GeForce 8
SM 3.0
SM 4.0
DirectX 9.0c
DirectX 10
Notes: Spill driver markedet

## Slide 3: Basic 3D Graphics Pipeline
Application
Scene Management
Geometry
Rasterization
Pixel Processing
ROP/FBI/Display
Frame
Buffer
Memory
Host
GPU
Notes: Geometry = Setter opp vertexer (kanter i triangler), og lager triangler
Rasterization = Finne ut hvilke pixler som hører hjemme i trianglet
Pixel = Manipulere, gjøre effekter med pixler
ROP = Render Out Put = Siste ”touch” på triangler, eller på AA, osv. Finner også ut om vi trenger pixlen (er den synlig (Hidden Surface Removal))

## Slide 4: Graphics in the PC Architecture
QuickPath (QPI) between processor and Northbridge (X58)
  Memory Control in CPU
Northbridge (IOH) handles PCI Express
  PCIe 2.0 x16 bandwidth at 16 GB/s (8 GB in each direction)
Southbridge (ICH10) handles all other peripherals
Notes: PCI Express = Seriel bus, flere kanaler…. 0,5 GB/sec hver vei
Mer strøm!
Snart PCI Express 3.0

## Slide 5: High-end Hardware
nVIDIA Fermi Architecture
The latest generation GPU, codenamed GF100
3,1 billion transistors
512 Processing cores (SP)
  IEEE 754-2008 Capable
  Shared coherent L2 cache
  Full C++ Support
  Up to 16 concurrent kernels
Notes: 40nm største hos TSMC

## Slide 6: Lab Hardware
nVidia GeForce GTX 280
Based on the GT200 chip
  1400 million transistors
  240 Processing cores (SP) at 1476MHz
  1024 MB Memory with 159 GB/sec bandwidth
nVidia GeForce 8800GT
Based on the G92 chip
  754 million transistors
  112 Processing cores (SP) at 1500MHz
  256 MB Memory with 57.6GB/sec bandwidth
Notes: Begge er Compute 1.1
En maskin med 8800GTX – Compute 1.0

## Slide 7: GeForce GF100 Architecture
Notes: A ”mile-high” overview

## Slide 8: nVIDIA GF100 vs. GT200 Architecture
Notes: TPC = Texture Processor Cluster
SM = Streaming Multiprocessor
SP = Stream Processor (Oppererer med Scalar-verdier)
SFU = Special Function Unit
TEX = Texturing Unit

## Slide 9: TPC… SM… SP… Some more details…
TPC
  Texture Processing Cluster
SM
  Streaming Multiprocessor
  In CUDA: Multiprocessor, and fundamental unit for a thread block
TEX
  Texture Unit
SP
  Stream Processor
  Scalar ALU for single CUDA thread
SFU
  Super Function Unit
TPC
TPC
TPC
TPC
TPC
TPC
TPC
TPC
TEX
SM
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Data L1
Texture Processor Cluster
Streaming Multiprocessor
SM
Shared Memory
SM
SM

## Slide 10: SP: The basic processing block
The nVIDIA Approach:
  A Stream Processor works on a single operation
AMD GPU’s work on up to five operations
Now, let’s take a step back for a closer look!

## Slide 11: Streaming Multiprocessor (SM)
Streaming Multiprocessor (SM)
  8 Streaming Processors (SP)
  2 Super Function Units (SFU)
Multi-threaded instruction dispatch
  1 to 1024 threads active
  Try to Cover latency of texture/memory loads
Local register file (RF)
16 KB shared memory
DRAM texture and memory access
Streaming Multiprocessor
(
SM
)
Store to
SP
0
RF
0
SP
1
RF
1
SP
2
RF
2
SP
3
RF
3
SP
4
RF
4
SP
5
RF
5
SP
6
RF
6
SP
7
RF
7
Constant L
1
Cache
L
1
Fill
Load from Memory
Load Texture
S
F
U
S
F
U
Instruction Fetch
Instruction L
1
Cache
Thread
/
Instruction Dispatch
L
1
Fill
Work
Control
Results
Shared Memory
Store to Memory
Foils adapted from nVIDIA

## Slide 12: SM Register File
Register File (RF)
  32 KB
  Provides 4 operands/clock
TEX pipe can also read/write Register File
  3 SMs share 1 TEX
Load/Store pipe can also read/write Register File
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU
Notes: TEX er mer viktig for grafikk

## Slide 13: Constants
Immediate address constants
Indexed address constants
Constants stored in memory, and cached on chip
  L1 cache is per Streaming Multiprocessor
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 14: Shared Memory
Each Stream Multiprocessor has 16KB of Shared Memory
  16 banks of 32bit words
CUDA uses Shared Memory as shared storage visible to all threads in a thread block
  Read and Write access
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 15: Execution Pipes
Scalar MAD pipe
  Float Multiply, Add, etc.
  Integer ops,
  Conversions
  Only one instruction per clock
Scalar SFU pipe
  Special functions like Sin, Cos, Log, etc.
    Only one operation per four clocks
TEX pipe (external to SM, shared by all SM’s in a TPC)
Load/Store pipe
  CUDA has both global and local memory access through Load/Store
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU
Notes: FMUL = Floating point multipler, FADD = Floating point add,
Hot clock/shader clock

## Slide 16: GPGPU
Foils adapted from nVIDIA

## Slide 17: What is really GPGPU?
General Purpose computation using GPU in other applications than 3D graphics
  GPU can accelerate parts of an application
Parallel data algorithms using the GPUs properties
  Large data arrays, streaming throughput
  Fine-grain SIMD parallelism
  Fast floating point (FP) operations
Applications for GPGPU
  Game effects (physics) nVIDIA PhysX
  Image processing (Photoshop CS4)
  Video Encoding/Transcoding (Elemental RapidHD)
  Distributed processing (Stanford Folding@Home)
  RAID6, AES, MatLab, etc.
Notes: Mark Harris, of Nvidia, runs the gpgpu.org website

## Slide 18: Previous GPGPU use, and limitations
Working with a Graphics API
  Special cases with an API like Microsoft Direct3D or OpenGL
Addressing modes
  Limited by texture size
Shader capabilities
  Limited outputs of the available shader programs
Instruction sets
  No integer or bit operations
Communication is limited
  Between pixels
Input Registers
Fragment Program
Output Registers
Constants
Texture
Temp Registers
per thread
per Shader
per Context
FB Memory

## Slide 19: nVIDIA CUDA
“Compute Unified Device Architecture”
General purpose programming model
  User starts several batches of threads on a GPU
  GPU is in this case a dedicated super-threaded, massively data parallel co-processor
Software Stack
  Graphics driver, language compilers (Toolkit), and tools (SDK)
Graphics driver loads programs into GPU
  All drivers from nVIDIA now support CUDA
  Interface is designed for computing (no graphics )
  “Guaranteed” maximum download & readback speeds
  Explicit GPU memory management

## Slide 20: Outline
The CUDA Programming Model
  Basic concepts and data types
The CUDA Application Programming Interface
  Basic functionality
An example application:
  The good old Motion JPEG implementation!
Notes: I dag skal skjelettet frem…. Om to uker blir det mer kjøtt på bena

## Slide 21: The CUDA Programming Model
The GPU is viewed as a compute device that:
  Is a coprocessor to the CPU, referred to as the host
  Has its own DRAM called device memory
  Runs many threads in parallel
Data-parallel parts of an application are executed on the device as kernels, which run in parallel on many threads
Differences between GPU and CPU threads
  GPU threads are extremely lightweight
    Very little creation overhead
  GPU needs 1000s of threads for full efficiency
    Multi-core CPU needs only a few

## Slide 22: Thread Batching: Grids and Blocks
A kernel is executed as a grid of thread blocks
  All threads share data memory space
A thread block is a batch of threads that can cooperate with each other by:
  Synchronizing their execution
    Non synchronous execution is very bad for performance!
  Efficiently sharing data through a low latency shared memory
Two threads from two different blocks cannot cooperate
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Notes: 1 kernel eksekverer 1 grid…
1 block kjører på 1 SM (Multiprosessor)

## Slide 23: CUDA Device Memory Space Overview
Each thread can:
  R/W per-thread registers
  R/W per-thread local memory
  R/W per-block shared memory
  R/W per-grid global memory
  Read only per-grid constant memory
  Read only per-grid texture memory
The host can R/W global, constant, and texture memories
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 24: Global, Constant, and Texture Memories
Global memory:
  Main means of communicating R/W Data between host and device
  Contents visible to all threads
Texture and Constant Memories:
  Constants initialized by host
  Contents visible to all threads
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host

## Slide 25: Terminology Recap
device = GPU = Set of multiprocessors
Multiprocessor = Set of processors & shared memory
Kernel = Program running on the GPU
Grid = Array of thread blocks that execute a kernel
Thread block = Group of SIMD threads that execute a kernel and can communicate via shared memory
Memory | Location | Cached | Access | Who
Local | Off-chip | No | Read/write | One thread
Shared | On-chip | N/A - resident | Read/write | All threads in a block
Global | Off-chip | No | Read/write | All threads + host
Constant | Off-chip | Yes | Read | All threads + host
Texture | Off-chip | Yes | Read | All threads + host

## Slide 26: Access Times
Register – Dedicated HW – Single cycle
Shared Memory – Dedicated HW – Single cycle
Local Memory – DRAM, no cache – “Slow”
Global Memory – DRAM, no cache – “Slow”
Constant Memory – DRAM, cached, 1…10s…100s of cycles, depending on cache locality
Texture Memory – DRAM, cached, 1…10s…100s of cycles, depending on cache locality

## Slide 27: CUDA – API

## Slide 28: CUDA Highlights
The API is an extension to the ANSI C programming language
Low learning curve than OpenGL/Direct3D
The hardware is designed to enable lightweight runtime and driver
High performance

## Slide 29: CUDA Device Memory Allocation
cudaMalloc()
  Allocates object in the device Global Memory
  Requires two parameters
    Address of a pointer to the allocated object
    Size of allocated object
cudaFree()
  Frees object from device Global Memory
    Pointer to the object
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host

## Slide 30: CUDA Device Memory Allocation
Code example:
  Allocate a 64 * 64 single precision float array
  Attach the allocated storage to Md.elements
  “d” is often used to indicate a device data structure
BLOCK_SIZE = 64;
Matrix Md
int size = BLOCK_SIZE * BLOCK_SIZE * sizeof(float);
cudaMalloc((void**)&Md.elements, size);
cudaFree(Md.elements);

## Slide 31: CUDA Host-Device Data Transfer
cudaMemcpy()
  memory data transfer
  Requires four parameters
    Pointer to source
    Pointer to destination
    Number of bytes copied
    Type of transfer
      Host to Host
      Host to Device
      Device to Host
      Device to Device
Asynchronous operations available (Streams)
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host

## Slide 32: CUDA Host-Device Data Transfer
Code example:
  Transfer a 64 * 64 single precision float array
  M is in host memory and Md is in device memory
  cudaMemcpyHostToDevice and cudaMemcpyDeviceToHost are symbolic constants
cudaMemcpy(Md.elements, M.elements, size, cudaMemcpyHostToDevice);
cudaMemcpy(M.elements, Md.elements, size, cudaMemcpyDeviceToHost);

## Slide 33: CUDA Function Declarations
 | Executed on the: | Only callable from the:
__device__ float DeviceFunc() | device | device
__global__ void KernelFunc() | device | host
__host__ float HostFunc() | host | host
__global__ defines a kernel function
  Must return void
__device__ and __host__ can be used together

## Slide 34: CUDA Function Declarations
__device__ functions cannot have their address taken
Limitations for functions executed on the device:
  No recursion
  No static variable declarations inside the function
  No variable number of arguments

## Slide 35: Some Information on the Toolkit

## Slide 36: Compilation
Any source file containing CUDA language extensions must be compiled with nvcc
nvcc is a compiler driver
  Works by invoking all the necessary tools and compilers like cudacc, g++, etc.
nvcc can output:
  Either C code
    That must then be compiled with the rest of the application using another tool
  Or object code directly

## Slide 37: Linking & Profiling
Any executable with CUDA code requires two dynamic libraries:
  The CUDA runtime library (cudart)
  The CUDA core library (cuda)
Several tools are available to optimize your application
  nVIDIA CUDA Visual Profiler
  nVIDIA Occupancy Calculator
Windows users: NVIDIA Parallel Nsight for Visual Studio

## Slide 38: Debugging Using Device Emulation
An executable compiled in device emulation mode (nvcc -deviceemu):
  No need of any device and CUDA driver
When running in device emulation mode, one can:
  Use host native debug support (breakpoints, inspection, etc.)
  Call any host function from device code
  Detect deadlock situations caused by improper usage of __syncthreads
nVIDIA CUDA GDB
printf is now available on the device! (cuPrintf)

## Slide 39: Before you start…
Four lines have to be added to your group users .bash_profile or .bashrc file
  PATH=$PATH:/usr/local/cuda/bin
  LD_LIBRARY_PATH=$LD_LIBRARY_PATH:/usr/local/cuda/lib
  export PATH
  export LD_LIBRARY_PATH
SDK is downloaded in the /opt/ folder
Copy and build in your users home directory

## Slide 40: Some usefull resources
nVIDIA CUDA Programming Guide 3.2
http://developer.download.nvidia.com/compute/cuda/3_2/toolkit/docs/CUDA_C_Programming_Guide.pdf
nVIDIA CUDA C Programming Best Practices Guide http://developer.download.nvidia.com/compute/cuda/3_2/toolkit/docs/CUDA_C_Best_Practices_Guide.pdf
nVIDIA CUDA Reference Manual 3.2
http://developer.download.nvidia.com/compute/cuda/3_2/toolkit/docs/CUDA_Toolkit_Reference_Manual.pdf

## Slide 41: Example:
Motion JPEG Encoding

## Slide 42: 14 different MJPEG encoders on GPU
Nvidia GeForce GPU
Problems:
Only used global memory
To much synchronization between threads
Host part of the code not optimized
Notes: Results from the course INF5063: Advanced course in programming heterogeneous architectures
Two assignments (home exams) on MJPEG (on Cell and GPU)
Y axis IS NOT at the SAME SCALE
one assignment “I/O bound” on the Cell
Looks like it was easy to get better performance on Nvidia GPU (more about this later)

## Slide 43: Profiling a Motion JPEG encoder on x86
A small selection of DCT algorithms:
  2D-Plain: Standard forward 2D DCT
  1D-Plain: Two consecutive 1D transformations with transpose in between and after
  1D-AAN: Optimized version of 1D-Plain
  2D-Matrix: 2D-Plain implemented with matrix multiplication
Single threaded application profiled on a Intel Core i5 750

## Slide 44: Optimizing for GPU, use the memory correctly!!
Several different types of memory on GPU:
  Global memory
  Constant memory
  Texture memory
  Shared memory
First Commandment when using the GPUs:
  Select the correct memory space, AND use it correctly!

## Slide 45: How about using a better algorithm??
Used CUDA Visual Profiler to isolate DCT performance
2D-Plain Optimized is optimized for GPU:
  Shared memory
  Coalesced memory access
  Loop unrolling
  Branch prevention
  Asynchronous transfers
Second Commandment when using the GPUs:
  Choose an algorithm suited for the architecture!

## Slide 46: Effect of offloading VLC to the GPU
VLC (Variable Length Coding) can also be offloaded:
  One thread per macro block
  CPU does bitstream merge
Even though algorithm is not perfectly suited for the architecture, offloading effect is still important!